## Slide 1: Potential activity of methanogens
Karoline W. Noer
Master student
Supervisors:
Niels Peter Revsbech and Lars D.M. Ottosen

## Slide 2: Goals
Estimate the potential activity of methanogens from anaerobic digesters
  Methane production with and without hydrogen addition
Develop a method to compare the upgrading potential of different anaerobic digesters
Notes: The goal of my studies is to develop an assay that will give a realistic and comparable estimate of the methanogenic activity in a anaerobic digester
I will evaluate the methane production rate with and without added hydrogen and compare it to the production in the reactor at the time of sampling.

## Slide 3: Potential activity assay
Collect material from anaerobic reactor
  Gas fast bag with argon, directly from reactor
Material is transferred into serum bottles flushed with argon.
Headspace is flushed with the specific gas mixture
Flasks are incubated in rotor at temperature of the reactor
Gas samples from the headspace is collected every 30min for 2h
Methane measurements, GC-FID
Notes: Basic procedure of potential activity assay
Evaluating and changing the assay continously
  Dilution
  Undiluted
  Gas composition

## Slide 4: Anaerobic digesters
Anaerobic digester
Viby WWTP
Mesophilic 38°C
Primary and secondary sludge
(bioslam)
Anaerobic digester
Åby WWTP
Thermophilic 49°C
Primary and secondary sludge (bioslam)
Mesophilic 39°C
Different waste and organic material from farms
Anaerobic digester
Bånlev Biogas

## Slide 5: Avoid mass transfer limitations - dilution of material
Dilution of the material from the digester with media (Pennings et al. 1998)
  1:10 dilution
Headspace
  H2/CO2 in 80:20 ratio
  N2 in control
Methane production over 2h
Methane production rate calculated from slope of linear regression
Chart: Viby WWTP, Methan production 3/12-2015
| 0 | 30 | 60 | 90 | 120
H2 rep.1 | 8.9902e-08 | 1.6633e-06 | 4.4893e-06 | 6.0308e-06 | 9.787e-06
H2 rep.2 | 2.9546e-07 | 1.8441e-06 | 3.7729e-06 | 5.4424e-06 | 7.9467e-06
H2 rep.3 | 1.9908e-07 | 2.499e-06 | 5.0531e-06 | 6.3806e-06
H2 rep.4 | -8.4825e-08 | 3.3814e-06 | 5.0772e-06 | 8.7304e-06 | 1.1881e-05
N2 rep.1 | 2.6659e-07 | 5.4659e-07 | 2.9324e-07 | 6.3053e-07 | 7.8768e-07
N2 rep.2 | 2.1821e-07 | 5.5907e-07 | 6.362e-07 | 1.0065e-06 | 1.1581e-06
N2 rep.3 | -1.3886e-09 | 1.2404e-07 | 1.4204e-07 | 2.8212e-07 | 4.8061e-07
N2 rep.4 | 1.8133e-07 | 8.7425e-07 | 7.9141e-07 | 9.7201e-07 | 8.3857e-07
Measurements from Viby WWTP, Åby WWTP and Bånlev Biogas
Notes: The first version of this experiment was where I diluted material from the reactor in a 1:10 ration with anaerobic media previously used for methanogens.
The serum bottle was flushed hydrogen/carbondioxide mixture 80% and 20%
The controle bottles was flushed with nitrogen. The trail with material from Viby to the right has 4 replica of the hydrogen/CO2 and controle.
As mentioned before the experiment is runned for 2h and gas samples from the headspace is taken every 30min.
From GC measurements the concentrations of methane in the headspace in the trail with viby material is seen in the graph.
Calculating the rate.
Done with material from anaerobic digesters at Viby WWTP, Åby WWTP and Bånlev biogas.

## Slide 6: Rates of diluted material
Faster production with H2/CO2
Rates far lower than in the reactor
Chemical environment?
Chart: Methane production rate
| H2/CO2 | N2 | Reactor | H2/CO2 | N2 | Reactor | H2/CO2 | N2 | Reactor
 | 0.31919 | 0.020541 | 0.3812 | 0.075104 | 0.025038 | 0.645 | 0.39682 | 0.043091 | 0.5184
100%
Notes: In the coloumn diagram to the right we see the methane production rates from trails with media diluted material from Viby, Åby and Bånlev.
In generel is the rate of the H2/CO2 samples higher than the controle samples (93%, 66%, 89%)
What is the reson for the low rates in the controles?
Chemical environment in the media? To big changes compared to in the reactor?
Try to dilute in saline water instead

## Slide 7: Dilution in 0.5%saline water
Same procedure, 0.5% KCl water
Dilution series
Rates still does not match
10mL material with H2/CO2 headspace shows high rates
Chart: 
| H2/CO2 | N2 | Reactor
Bånlev 14-01-2016 | 0.15937 | 0.0027248 | 0.7964
Chart: Dilution in 0.5% saline water, and 10mL pure material
| 10mL | 5mL | 1mL | N2, 5mL | Reactor
dilution in water | 0.89654 | 0.45274 | 0.20423 | 0.1632 | 0.3812
Chart: Viby 15-12-2015
| H2/CO2, 1mL | N2, 1mL | H2/CO2, 10mL | N2, 10mL | Reactor
dilute | 0.21333 | 0.035566 | 0.54825 | 0.17881 | 0.3812
100%
235%
Notes: Dilution in 0.5% kaliumchlorid dilution
Rates are still lower than in the reactor, and basicly the same rates as dilute in pennings, nothing really happens, very small amount of methane is produced test the volumen af material. As seen the larger amounts of material gives substantial higher rates, eventhough the controle is still lower than the reactor potential (but closer).
I tried to make a dilution series to

## Slide 8: Test of dilution/undiluted
10mL pure material
1.5bar H2/CO2 or N2/CO2
Final pH*:
  H2/CO2: ~9.50
  N2/CO2: ~ 8.97
*after 3 days incubation
Methane production with different amount of material
10mL undiluted material with N2/CO2 closest to reactor levels
Chart: Methane production
| N2, 1mL | N2, 5mL | N2, 10mL | N2/CO2, 10mL | Reactor, Bånlev | Reactor, Viby
 | 0.035566 | 0.1632 | 0.17881 | 0.84697 | 0.8104 | 0.3812
Chart: Methane production rate, 1.5bar
| H2/CO2, 10mL | N2/CO2, 10mL | Reactor
1.5bar | 13.0459 | 0.84697 | 0.8104
9% | 43% | 47% | 105% | 100% | 100%
Notes: Tried with undiluted material, under pressure (1.5bar)  plenty of gas
Added CO2 to the controle to keep pH in material
High rates
Is it the added CO2?

## Slide 9: CO2 series
Buffer with phosphate buffer
  Minimize the pH effect
Same procedure
N2/CO2 with different CO2 concentrations
Not up to reactor rates
Same with 0.02M acetate
CO2 do not seem to effect rate
Chart: CO2 serie
| 0 | 0.01 | 0.12 | 0.27 | 0.66 | 1
 | 0.095935 | 0.18967 | 0.19945 | 0.1207 | 0.087741 | 0.12581
Chart: CO2 serie, with acetate
| Ac., 0% | Ac., 1% | Ac., 12% | Ac., 27% | Ac., 66% | Ac., 100%
 | 0.45481 | 0.35897 | 0.39708 | 0.078486 | 0.11849 | 0.21583
Chart: CO2 series, Bånlev material
| Ac., 0% | Ac., 1% | Ac., 12% | Ac., 27% | Ac., 66% | Ac., 100% | Reactor
CO2 serie | 0.095935 | 0.18967 | 0.19945 | 0.1207 | 0.087741 | 0.12581
CO2 serie with acetate | 0.45481 | 0.35897 | 0.39708 | 0.078486 | 0.11849 | 0.21583 | 0.8466
11%
Notes: Series with different CO2 concentrations
Add phosphate buffer to keep the pH from reaching inhibiting values
Acetate was also added to investigate if the low rates is due to low acetate concentration (as it is quickly depleeted when stopped feeding)
Lower rates than in the reactor. No clear patteren.

## Slide 10: Next
Potential activity assay with 10mL pure material from different anaerobic digesters
Test the effect of VS concentration in reactor on the assay